## Slide 1: Girls into Coding activity 3 images

## Slide 2: Image 1
We can close these instructions for the moment, we won’t use them yet for this activity! We will take a look at them later on !
This is our robot ! 
These yellow spots are the robot’s ultrasonic distance sensors!!

## Slide 3: Image 2
[1] Right click on the robot
[2] Click: Edit controller

## Slide 4: Image 3
[1] We should end up with the new code pasted in the controller window
[2] Click the menu icon, then -> Save
[3] Reset simulation
[4] Start simulation

## Slide 5: Image 5
[2] We should see this window pop up! We can see our messages from the robot here
[4] Start the simulation
[3] Reset the simulation
[1] Click console
[5] Have a look at how the messages change as the robot approaches the wall!

## Slide 6: Image 6
Distance (meters)
Direction
0
1
1.5
0.5
-0.5
-1.5
-2.5
-3.5
Right
Left
How we measure object location using the ultrasonic sensors!
0.5
1.5
2.5
3.5

## Slide 7: Image 7
Start
Go forwards
Go Backwards
Turn right
0
Object detected
No object detected
Less than 2 seconds passed
2 seconds passed
2 seconds passed
Less than 2 seconds passed
1
2
Key
State
name
Robot state number
Transition condition
Our finite state machine  !
It’s not complicated once we talk about it !

## Slide 8: Image 8
If wall detected then:
robotState =1
If backwards movement finished then:
robotState =2
If turn movement finished then:
robotState =0
Switcher(robotState):
If robotState == 0:
goForwards()
If robotState == 1:
goBackwards()
If robotState == 2:
turnRight()
Transition conditions in functions
Our pseudo code for a state machine  !
It’s not complicated once we talk about it !
Loop forever!
Never ending loop

## Slide 9: Image 9
Start
Go forwards
Go Backwards
Turn right
0
Object detected
No object detected
Less than 2 seconds passed
2 seconds passed
2 seconds passed
Less than 2 seconds passed
1
2
Key
State
name
Robot state number
Transition condition
Our new finite state machine  !
It’s not complicated once we talk about it !